## Slide 1
AUTOMATIC STREET LIGHT
USING LDR
A simple light-sensitive transistor switching circuit
Electronic Devices and Circuits | ECE
Name: ____________________ Register No.: ____________________
Simple low-cost light-sensing automation project

## Slide 2
1. Introduction
• An automatic street light switches ON when the surroundings become dark.
• It switches OFF when sufficient light falls on the sensor.
• The circuit uses an LDR, a transistor, resistors and an LED.
• It demonstrates sensing and electronic switching.
2

## Slide 3
2. Aim and Objectives
• Aim: To design and simulate an automatic street-light circuit using an LDR.
• Detect changes in ambient light using the LDR.
• Use an NPN transistor as an electronic switch.
• Reduce unnecessary lighting during daytime.
3

## Slide 4
3. Components Required
• LDR (light-dependent resistor) — senses light intensity.
• NPN transistor (for example, 2N2222) — switches the LED.
• Resistors: 10 kΩ for the sensor divider/base path and 220 Ω for LED current limiting.
• LED, 5 V DC supply, breadboard and connecting wires.
Use the exact component names available in the Tinkercad component panel.
4

## Slide 5
4. Circuit Connection
• Connect +5 V to a 10 kΩ resistor; connect its other end to the BASE node.
• Connect the LDR between the BASE node and GND.
• Connect the transistor EMITTER to GND.
• Connect +5 V → 220 Ω resistor → LED anode; LED cathode → transistor COLLECTOR.
• Keep all grounds connected to the same GND rail.
Check the transistor pinout in Tinkercad before wiring; pin order depends on the model.
5

## Slide 6
5. Circuit Diagram (conceptual)
+5 V
220 Ω + LED
NPN transistor
GND
10 kΩ resistor
BASE node
LDR
GND (common)
Concept: the LDR connects from the base node to ground. In darkness its resistance rises, allowing the base node to rise and turn the transistor ON.
6

## Slide 7
6. Working Principle
• An LDR has lower resistance in bright light and higher resistance in darkness.
• In daylight, the LDR pulls the base node low; the transistor remains OFF and the LED is OFF.
• In darkness, the LDR resistance increases; the base node rises through the 10 kΩ resistor.
• The transistor turns ON and current flows through the LED, so it lights up.
7

## Slide 8
7. Software Simulation Procedure
• Open tinkercad.com and sign in; select Circuits → Create new Circuit.
• Place an LDR, NPN transistor, LED, resistors and a 5 V supply.
• Wire the circuit using the connection list and check transistor pinout.
• Start Simulation and change the LDR light level if the component supports it.
• Observe the LED in bright and dark conditions; capture screenshots for the report.
8

## Slide 9
8. Applications, Advantages and Limitations
• Applications: streetlights, garden lights, pathway lights and automatic night lamps.
• Advantages: simple, low cost, automatic operation and easy maintenance.
• Limitations: sensor response can be affected by shadows, dust and nearby lights.
• A practical outdoor system may need a relay/driver stage and weatherproof housing.
9

## Slide 10
9. Result and Conclusion
• The proposed circuit demonstrates automatic LED switching based on ambient light.
• Bright condition: transistor OFF and LED OFF.
• Dark condition: transistor ON and LED ON.
• The project explains LDR characteristics and the use of a transistor as a switch.
Report actual simulation observations; add your own Tinkercad screenshots before submission.
10

## Slide 11
10. References
• Tinkercad Circuits — https://www.tinkercad.com/
• Electronic Devices and Circuits class notes: LDR characteristics and transistor switching.
• Component datasheets for the selected LDR and NPN transistor.
Thank you
11